## Slide 1
COURSE: COMPUTER ARCHITECTURE
Introduction to Computer Architecture
Lecture 1 — Overview, History, Fundamental Blocks, Cost & Performance
Duration: 60 minutes
Reference: Patterson & Hennessy, Computer Organization and Design (4th Ed.), Ch. 1

## Slide 2
Today's Agenda
Four building blocks for your first hour in Computer Architecture
01
Overview & History
What is computer architecture, and how did we get here?
02
Fundamental Blocks
The five classic components of any computer
03
Cost Factor
Why cost drives real-world design decisions
04
Performance Metrics
How we measure and compare computer performance
Computer Architecture · Lecture 1
2

## Slide 3
What Is Computer Architecture?
Two connected layers
Computer Architecture = the attributes visible to a programmer: instruction set, addressing, data types.
Computer Organization = how those attributes are actually implemented in hardware (datapath, control, memory).
This course studies both — the hardware/software interface.
The field constantly balances performance, cost, power, and reliability.
A Very Short History
1940s
Vacuum tubes — first electronic computers (ENIAC)
1950s–60s
Transistors & integrated circuits shrink hardware
1970s–80s
Microprocessors bring computing to the desktop
2000s
Power wall halts clock-speed race
Today
Multicore & multiprocessor systems dominate
Computer Architecture · Lecture 1
3

## Slide 4
Fundamental Blocks of a Computer
Five classic hardware components — every computer has these
Input
Devices that bring data/instructions in
Output
Devices that deliver results out
Memory
Stores programs and data
Datapath
Performs arithmetic/logic operations
Control
Directs the datapath, memory & I/O
Key idea: The datapath and control together are often called "the processor." Memory holds both instructions and data — the stored-program concept.
Computer Architecture · Lecture 1
4

## Slide 5
The Cost Factor
Why cost—not just speed—drives architecture decisions
Integrated Circuit Cost
Cost per die rises sharply as die size increases (yield falls with area).
Cost per wafer and defect rate together determine die cost.
High-volume production lowers cost per chip — fixed engineering costs are spread out.
Learning curve: cost drops as manufacturing experience grows over a technology's lifetime.
Performance per Unit Cost — Across Eras
Vacuum Tube
1×
Transistor
35×
Integrated Circuit (SSI)
900×
VLSI (Microprocessor)
400,000×
Bar length shown on a log scale (orders of magnitude), not linear.
Computer Architecture · Lecture 1
5

## Slide 6
Performance Metrics
How do we measure "how fast" a computer really is?
Response Time
Time between start and completion of a task (latency).
Throughput
Total amount of work done per unit time.
CPU Time
CPU clock cycles × Clock cycle time, for a program.
CPI
Clock cycles Per Instruction — cost of each instruction type.
The Core Performance Equation
CPU Time = Instruction Count × CPI × Clock Cycle Time
The three variables designers can influence — architecture, compiler, and technology each affect a different one.
Rule of thumb: "X is n times faster than Y" means Execution Time(Y) / Execution Time(X) = n.
Computer Architecture · Lecture 1
6

## Slide 7
Where to Read More
Patterson & Hennessy — Computer Organization and Design, 4th Edition
Today's Topic | Book Section | Pages
Overview & History of Computer Architecture | Ch.1 — §1.1 Introduction, §1.10 Historical Perspective | 3–9, 55–72
Fundamental Blocks (Input, Output, Memory, Datapath, Control) | Ch.1 — §1.3 Under the Covers | 13–26
Cost Factor (IC manufacturing cost, cost/performance) | Ch.1 — §1.6 & Elaboration on IC Cost; §1.7 Real Stuff | 41–51
Performance Metrics (response time, throughput, CPU time, CPI) | Ch.1 — §1.4 Performance | 26–39
Also useful for cost/I-O sections: William Stallings, Computer Organization and Architecture (parallel treatment, easier prose).
Computer Architecture · Lecture 1
7

## Slide 8
Recap & What's Next
Computer architecture links programmer-visible attributes to hardware organization.
Every computer shares five fundamental blocks: input, output, memory, datapath, control.
Cost and performance are always in tension — cost/performance drives real design choices.
Performance is measured via response time, throughput, CPU time, and CPI.
Next Class:
Instruction Set Architecture — RISC vs. CISC, ARM & x86 (Ch. 2 & Appendix)
Computer Architecture · Lecture 1
8