## Slide 1
COURSE: COMPUTER ARCHITECTURE
Instruction Set Architecture: RISC, CISC, x86 & ARM
Lecture 2 — Classifying ISAs, Registers, Addressing Modes, RISC vs. CISC
Duration: 60 minutes
Reference: Patterson & Hennessy, Computer Organization and Design (4th Ed.), Ch. 2 & Appendix E

## Slide 2
Today's Agenda
Four building blocks for your second hour in Computer Architecture
01
Classifying ISAs & Registers
How instructions access operands, and why registers matter
02
Addressing Modes
Five ways an instruction can locate its operands
03
RISC vs. CISC
Two philosophies of instruction set design
04
x86 & ARM Architecture
Real-world ISAs powering desktops and mobile devices
Computer Architecture · Lecture 2
2

## Slide 3
Classifying Instruction Set Architectures
How instructions access their operands — and why registers matter
Operand Storage: Four Classes
Stack Architecture
Operands are implicit, taken from the top of a stack (e.g., early HP calculators).
Accumulator Architecture
One operand is implicit, held in a single accumulator register (early computers).
Register-Memory Architecture
One operand in a register, one directly in memory (x86).
Register-Register (Load-Store)
All operands in registers; memory is touched only via load/store (MIPS, ARM, RISC-V).
Why Registers Matter
Registers are much faster to access than memory — no memory latency.
There are only a few registers, so compilers can allocate them efficiently.
MIPS has 32 general-purpose registers ($0–$31), each 32 bits wide.
$zero is hardwired to 0; others follow naming conventions ($sp, $ra, $t0–$t9, $s0–$s7).
Key idea: Most modern general-purpose ISAs (MIPS, ARM, RISC-V) are register-register / load-store — memory is touched only by explicit load and store instructions.
Computer Architecture · Lecture 2
3

## Slide 4
Addressing Modes
Five ways a MIPS instruction can locate its operands
Register
Operand is a register's value.
add $t0, $t1, $t2
Immediate
Operand is a constant in the instruction.
addi $t0, $t1, 4
Base / Displacement
Address = register + constant offset.
lw $t0, 8($sp)
PC-Relative
Branch target = PC + offset (words).
beq $t0, $t1, target
Pseudodirect
Jump target from PC's top bits + address field.
j target
Key idea: The addressing mode determines how the effective operand or memory address is computed — richer modes generally mean more complex (and slower) decode hardware.
Computer Architecture · Lecture 2
4

## Slide 5
RISC vs. CISC
Two philosophies of instruction set design
RISC
Reduced Instruction Set Computer
Simple, fixed-length instructions
Few addressing modes
Only load/store instructions touch memory
Many general-purpose registers
Leans on the compiler & pipelining for speed
Examples: MIPS, ARM, RISC-V, SPARC, PowerPC
CISC
Complex Instruction Set Computer
Variable-length, multi-operation instructions
Many addressing modes
Instructions can operate directly on memory
Fewer, more specialized registers historically
Relies on microcode for complex instructions
Examples: x86, x86-64, VAX, IBM 360/370
Computer Architecture · Lecture 2
5

## Slide 6
x86 & ARM Architecture
Two real-world ISAs that shape modern computing
x86 Origins
Intel 8086 (1978); CISC heritage; became the desktop & server standard.
x86 Today
x86-64 extends to 64-bit; deep pipelines; translates CISC ops into RISC-like micro-ops.
ARM Origins
Acorn RISC Machine (1985); RISC design from day one; built for low power.
ARM Today
Powers most phones & tablets; ARMv8-A adds a 64-bit mode (AArch64).
Design Trade-off
x86 emphasizes backward compatibility and raw single-thread performance. ARM emphasizes energy efficiency and simplicity. The same trade-offs seen in RISC vs. CISC design now shape the split between mobile and desktop computing.
Computer Architecture · Lecture 2
6

## Slide 7
Where to Read More
Patterson & Hennessy — Computer Organization and Design, 4th Edition
Today's Topic | Book Section | Pages
Classifying ISAs & Registers | Ch. 2 — §2.1 Introduction, §2.3 Operands of the Computer Hardware | 76, 80–86
Addressing Modes | Ch. 2 — §2.10 MIPS Addressing for 32-Bit Immediates and Addresses | 128–137
RISC vs. CISC | Appendix E — §E.1 Introduction, §E.2 Addressing Modes and Instruction Formats | E-3–E-9
x86 & ARM Architecture | Ch. 2 — §2.16 Real Stuff: ARM Instructions; §2.17 Real Stuff: x86 Instructions | 161–174
Also useful: Appendix E.3–E.16 surveys addressing modes and instructions across MIPS, ARM, SPARC, and PowerPC — a handy cross-vendor comparison.
Computer Architecture · Lecture 2
7

## Slide 8
Recap & What's Next
Instruction sets are classified by where operands live: stack, accumulator, register-memory, or register-register (load-store).
MIPS uses five addressing modes: register, immediate, base/displacement, PC-relative, and pseudodirect.
RISC favors simplicity and speed; CISC favors instruction richness and code density — modern x86 blends both internally.
x86 (CISC-rooted, desktop/server) and ARM (RISC-rooted, mobile/embedded) are the two dominant real-world ISAs today.
Next Class:
Memory Hierarchy — Cache Organization, Mapping & Replacement Policies (Ch. 5)
Computer Architecture · Lecture 2
8