## Slide 1
COURSE: COMPUTER ARCHITECTURE
Memory Hierarchy: Locality, Cache Structure & Mapping
Lecture 3 — Hierarchical Organization, Cache Basics, Mapping Techniques, Performance
Duration: 60 minutes
Reference: Patterson & Hennessy, Computer Organization and Design (4th Ed.), Ch. 5 §5.1–5.3

## Slide 2
Today's Agenda
Four building blocks for your third hour in Computer Architecture
01
Memory Hierarchy & Locality
Why we build a pyramid of memories, and the principle that makes it work
02
Cache Memory Basics
Tags, valid bits, and the anatomy of a direct-mapped cache
03
Cache Mapping Techniques
Direct-mapped, set-associative, and fully associative placement
04
Measuring Cache Performance
Hit rate, miss rate, and average memory access time
Computer Architecture · Lecture 3
2

## Slide 3
Memory Hierarchy & the Principle of Locality
Why programmers get the illusion of memory that is both large and fast
Four Levels of the Hierarchy
Registers
Fastest, smallest storage; built into the processor and holds values in active use.
Cache (SRAM)
Closest level outside the processor; small, fast, and expensive per bit.
Main Memory (DRAM)
Larger and slower than cache; holds the active program and its data.
Secondary Storage (Disk / Flash)
Largest and slowest level; holds everything not currently in use.
Why Memory Hierarchy Works
Temporal locality: if an item is referenced, it will tend to be referenced again soon.
Spatial locality: if an item is referenced, nearby items will tend to be referenced soon.
Programs access only a small portion of their address space at any instant of time.
Faster memories cost more per bit, so they are kept small and close to the processor.
Key idea: A memory hierarchy exploits locality of reference — keeping recently and nearby used data in fast, small memory near the processor gives the illusion of memory that is both large and fast.
Computer Architecture · Lecture 3
3

## Slide 4
Cache Memory Basics
The anatomy of a direct-mapped cache — how it finds and verifies data
Valid Bit
Marks whether a cache entry currently holds meaningful data.
V = 1 means valid
Tag
Upper address bits stored to confirm this is the requested block.
Tag == address bits?
Index
Selects which cache location to check; width = log2(number of blocks).
8 blocks → 3-bit index
Block Offset
Selects the byte or word within the block once it is found.
width = log2(block size)
Data
The actual instruction or data words copied in from memory.
One or more words
Key idea: Direct-mapped placement: (Block address) modulo (Number of blocks in the cache). The index alone picks the location; the tag then confirms it is really the requested block.
Computer Architecture · Lecture 3
4

## Slide 5
Cache Mapping Techniques
Where can a memory block go in the cache?
Direct-Mapped
Each block maps to exactly one cache location
(Block address) mod (number of blocks) picks the location
Only one comparator is needed per access
Simple, fast hardware — the classic baseline design
Conflict misses occur when two active blocks share a slot
No replacement decision — the resident block is always evicted
Example use: simple embedded and small L1 caches
Associative (Set / Fully)
A block maps to a set of n possible locations
(Block address) mod (number of sets) picks the set
n comparators search the set in parallel
Lower miss rate than direct-mapped at the same size
Needs a replacement policy to choose within the set
Fully associative is the extreme case: one set holds every block
Example use: most modern L1/L2 caches (2- to 16-way)
Computer Architecture · Lecture 3
5

## Slide 6
Measuring Cache Performance
How well is the cache actually working?
Hit Rate
Fraction of memory accesses found in the cache — a hit.
Miss Rate
1 − hit rate; the fraction of accesses that must go further down the hierarchy.
Miss Penalty
Extra clock cycles needed to fetch a block from the next level down.
AMAT
Average Memory Access Time — the true cost of a typical memory access.
AMAT Formula
Average memory access time = Hit time + Miss rate × Miss penalty. Worked example: hit time 1 cycle, miss rate 5%, miss penalty 20 cycles → AMAT = 1 + (0.05 × 20) = 2 cycles per access.
Computer Architecture · Lecture 3
6

## Slide 7
Where to Read More
Patterson & Hennessy — Computer Organization and Design, 4th Edition
Today's Topic | Book Section | Pages
Memory Hierarchy & Locality | Ch. 5 — §5.1 Introduction | 452–457
Cache Memory Basics | Ch. 5 — §5.2 The Basics of Caches | 457–466
Cache Mapping Techniques | Ch. 5 — §5.3 Measuring & Improving Cache Performance (Associativity) | 479–483
Measuring Cache Performance | Ch. 5 — §5.3 Measuring and Improving Cache Performance | 475–479, 492
Also useful: Section 5.5, A Common Framework for Memory Hierarchies, ties these ideas together across every level of the hierarchy.
Computer Architecture · Lecture 3
7

## Slide 8
Recap & What's Next
A memory hierarchy exploits temporal and spatial locality to give the illusion of memory that is both large and fast.
A direct-mapped cache uses tag, index, and valid-bit fields; block address mod number of blocks picks the location.
Placement ranges from direct-mapped to fully associative, with set-associative as the practical middle ground.
Cache performance is measured by hit rate, miss rate, and AMAT = hit time + miss rate × miss penalty.
Next Class:
Replacement Policies, Writing to a Cache & Main Memory (Ch. 5 cont.)
Computer Architecture · Lecture 3
8