## Slide 1
COURSE: COMPUTER ARCHITECTURE
Cache Optimization: Replacement, Writing & Main Memory
Lecture 4 — Replacement Policies, Writing to a Cache, Multilevel Caches, Main Memory
Duration: 60 minutes
Reference: Patterson & Hennessy, Computer Organization and Design (4th Ed.), Ch. 5 §5.2–5.3

## Slide 2
Today's Agenda
Four building blocks for your fourth hour in Computer Architecture
01
Replacement Policies
Choosing which block to evict when the cache is full
02
Writing to a Cache
Keeping cache and memory consistent on a store
03
Multilevel & Upgrading Caches
Adding cache levels to shrink the effective miss penalty
04
Main Memory
DRAM technology and organizing memory to feed the cache
Computer Architecture · Lecture 4
2

## Slide 3
Choosing Which Block to Replace
Cache is full — which resident block makes way for the new one?
Four Replacement Strategies
Least Recently Used (LRU)
Evicts the block that has gone longest untouched — tracks recency per set.
First-In, First-Out (FIFO)
Evicts the block that has been resident longest, regardless of recent use.
Random
Picks a victim at random — simple hardware, surprisingly competitive.
Optimal (Belady's)
Evicts the block used furthest in the future — a theoretical best case only.
Why Replacement Only Matters for Associative Caches
Direct-mapped caches have only one possible location per block, so there is nothing to choose.
Set-associative and fully associative caches offer n candidates per set — a policy is needed.
LRU tracks usage with reference bits or counters; cost grows fast with associativity.
As associativity increases beyond 4–8 ways, most designs approximate LRU rather than track it exactly.
Key idea: LRU exploits temporal locality directly: the block least likely to be reused soon is the one least recently used — but true LRU is expensive to implement exactly at high associativity, so real hardware often approximates it.
Computer Architecture · Lecture 4
3

## Slide 4
Writing to a Cache
Keeping cache and memory consistent when a store occurs
Write-Through
Every store updates both the cache and main memory immediately.
Simple, but memory traffic is high
Write-Back
Stores update only the cache; memory is updated when the block is replaced.
Needs a dirty bit
Write Allocate
On a write miss, the block is first loaded into the cache, then updated.
Pairs naturally with write-back
No-Write-Allocate
On a write miss, the block is written straight to memory, bypassing the cache.
Pairs naturally with write-through
Write Buffer
Holds pending writes so the processor doesn't stall waiting for memory.
Smooths write-through traffic
Key idea: Write-back minimizes memory traffic and pairs with write-allocate; write-through keeps memory always current and pairs with no-write-allocate — most real caches use write-back with write-allocate for performance.
Computer Architecture · Lecture 4
4

## Slide 5
Multilevel & Upgrading a Cache
Adding cache levels to shrink the effective miss penalty
Single-Level Cache (L1)
One cache sits between the processor and main memory
Hit time is fast, but every miss pays the full main-memory penalty
Miss penalty can be 100+ cycles on modern systems
Simple to design, verify, and reason about
Miss rate is bounded by the size of that one cache
Larger L1 caches slow down hit time, limiting how big L1 can grow
Example use: simple embedded microcontrollers
Multilevel Cache (L1-L3)
A second, larger cache sits between L1 and main memory
L1 stays small and fast; L2 catches most of L1's misses
Global miss penalty falls even though L1 alone is unchanged
AMAT extends naturally: MissPenalty(L1) = HitTime(L2) + MissRate(L2) × MissPenalty(L2)
Each level can use a different design — smaller/faster L1, larger/associative L2
"Upgrading a cache" often means adding or enlarging one of these levels
Example use: nearly all modern desktop and server processors (L1/L2/L3)
Computer Architecture · Lecture 4
5

## Slide 6
Main Memory & DRAM Technology
Feeding the cache from a slower, denser layer of memory
DRAM
Dynamic RAM — one transistor and one capacitor per bit; dense but must be refreshed.
SRAM
Static RAM — six transistors per bit; faster and more expensive, used for caches.
SDRAM / DDR
Synchronous DRAM clocked with the memory bus; DDR transfers on both clock edges.
Memory Interleaving
Splitting memory into banks that can be accessed in parallel to raise bandwidth.
Wider Memory, Faster Refills
Miss penalty = Memory access time × (Block size / Bus width). Worked example: a 4-word block, 1-word-wide bus, 15 cycles per access → 4 × 15 = 60 cycles. Widening the bus to 4 words cuts this to a single 15-cycle access.
Computer Architecture · Lecture 4
6

## Slide 7
Where to Read More
Patterson & Hennessy — Computer Organization and Design, 4th Edition
Today's Topic | Book Section | Pages
Replacement Policies | Ch. 5 — §5.3 Measuring & Improving Cache Performance (Choosing Which Block to Replace) | 484–486
Writing to a Cache | Ch. 5 — §5.2 The Basics of Caches (Handling Writes) | 466–470
Multilevel & Upgrading Caches | Ch. 5 — §5.3 Measuring & Improving Cache Performance (Multilevel Caches) | 487–491
Main Memory | Ch. 5 — §5.2 The Basics of Caches (Designing the Memory System to Support Caches) | 453–456, 471–478
Also useful: Section 5.10, Real Stuff: the AMD Opteron X4 and Intel Nehalem Memory Hierarchies, shows these techniques combined in production processors.
Computer Architecture · Lecture 4
7

## Slide 8
Recap & What's Next
Replacement policies decide which block leaves an associative cache — LRU exploits temporal locality, though hardware often approximates it.
Write-through keeps memory always current; write-back defers updates and needs a dirty bit — most systems pair write-back with write-allocate.
Multilevel caches (L1/L2/L3) let a small, fast L1 be backed by a larger L2 that absorbs most of its misses, lowering the effective miss penalty.
Main memory is built from DRAM; wider buses, interleaving, and DDR signaling all raise the bandwidth available to refill a cache line.
Next Class:
Virtual Memory — Paging, Address Translation & the TLB (Ch. 5 §5.4)
Computer Architecture · Lecture 4
8