## Slide 1
COURSE: COMPUTER ARCHITECTURE
Data Representation: Numbers, Floating-Point & Characters
Lecture 6 — Data Types, Signed Numbers, Floating-Point, Character Encoding
Duration: 60 minutes
Reference: Patterson & Hennessy, Computer Organization and Design (4th Ed.), Ch. 2 §2.4, 2.9; Ch. 3 §3.5

## Slide 2
Today's Agenda
Four building blocks for your sixth hour in Computer Architecture
01
Data Representation Fundamentals
How bits become bytes, words, and typed values
02
Signed & Unsigned Numbers
Encoding integers, and where two's complement comes from
03
Floating-Point Representation
Trading range and precision to represent real numbers
04
Character Representation
Encoding text as numbers, from ASCII to Unicode
Computer Architecture · Lecture 6
2

## Slide 3
Data Representation Fundamentals
Every value in a computer is ultimately a pattern of bits
Four Building Blocks of Data
Bit
The smallest unit of information — a single 0 or 1.
Byte
Eight bits, the smallest addressable unit of memory on most machines.
Word
The natural unit a processor operates on — 32 bits on MIPS, often 64 bits today.
Data Type
The interpretation applied to a bit pattern — integer, float, character, or address.
Why Representation Choices Matter
The same bit pattern means different things depending on its declared data type.
Fixed-width encodings trade range for a small, constant, predictable storage size.
Endianness determines whether the most- or least-significant byte is stored first.
Choosing a representation is a trade-off among range, precision, and hardware cost.
Key idea: A bit pattern has no inherent meaning — it is data only in the context of the type the hardware or program assigns to it: the same 32 bits can be an integer, a float, an instruction, or four characters.
Computer Architecture · Lecture 6
3

## Slide 4
Signed & Unsigned Numbers
Five ways (and formats) to encode integers in fixed-width binary
Unsigned Binary
Every bit contributes a positive power of two; range 0 to 2^n − 1.
1101 → 13
Sign-Magnitude
The top bit is a sign flag; the rest is the magnitude.
1101 → −5
One's Complement
Negative numbers are the bitwise complement of the positive value.
1101 → −2
Two's Complement
Invert and add 1; used by virtually every modern processor, including MIPS.
1101 → −3
Overflow
Occurs when a result falls outside the representable range for the format and width.
Adding two positives yielding a negative
Key idea: Two's complement dominates because it needs only one representation of zero, addition and subtraction reuse the same hardware as unsigned numbers, and sign-extension is simple — the top bit carries negative weight: −2^(n−1).
Computer Architecture · Lecture 6
4

## Slide 5
Floating-Point Representation
IEEE 754 trades a fixed bit budget between range and precision
Single Precision (32-bit)
1 sign bit, 8 exponent bits, 23 fraction (mantissa) bits
Exponent bias of 127, giving a wide practical range
About 7 decimal digits of precision
Range roughly ±1.4 × 10⁻⁴⁵ to ±3.4 × 10³⁸
Value = (−1)^S × 1.Fraction × 2^(Exponent − 127)
Smaller footprint — used when memory or bandwidth is tight
Example use: graphics, embedded, and machine-learning inference
Double Precision (64-bit)
1 sign bit, 11 exponent bits, 52 fraction (mantissa) bits
Exponent bias of 1023, giving a far larger range
About 15–16 decimal digits of precision
Range roughly ±4.9 × 10⁻³²⁴ to ±1.8 × 10³⁰⁸
Value = (−1)^S × 1.Fraction × 2^(Exponent − 1023)
Larger footprint — used when accuracy must be preserved over many operations
Example use: scientific computing and most general-purpose software
Computer Architecture · Lecture 6
5

## Slide 6
Character Representation
Encoding text as numbers, one code point at a time
ASCII
7-bit code assigning 128 values to letters, digits, punctuation, and control codes.
Extended ASCII
8-bit variants add 128 more codes for accented letters and symbols — not standardized.
Unicode
A single standard assigning a unique code point to characters from virtually every writing system.
UTF-8
Encodes Unicode using 1–4 bytes per character; backward-compatible with 7-bit ASCII.
ASCII in Practice
'A' = 65, 'a' = 97 — cases differ by exactly 32. '0' = 48, so a digit character minus 48 gives its numeric value. Space = 32. Strings in C are stored as bytes terminated by a null byte (0).
Computer Architecture · Lecture 6
6

## Slide 7
Where to Read More
Patterson & Hennessy — Computer Organization and Design, 4th Edition
Today's Topic | Book Section | Pages
Data Representation Fundamentals | Ch. 3 — §3.1 Introduction | 224–226
Signed & Unsigned Numbers | Ch. 2 — §2.4 Signed and Unsigned Numbers | 87–93
Floating-Point Representation | Ch. 3 — §3.5 Floating Point | 242–269
Character Representation | Ch. 2 — §2.9 Communicating with People | 122–127
Also useful: Section 3.7, Real Stuff: Floating Point in the x86, and Section 2.20 Historical Perspective connect these encodings to real instruction sets.
Computer Architecture · Lecture 6
7

## Slide 8
Recap & What's Next
All data is ultimately bits; a data type is the interpretation applied to a fixed-width pattern of them.
Two's complement is the standard signed integer format because it shares hardware with unsigned addition and has a single representation of zero.
IEEE 754 floating-point encodes sign, exponent, and fraction; single precision trades range and precision for a smaller footprint than double precision.
Character data is just another encoding — ASCII maps 128 values to text, and Unicode/UTF-8 extend that to the world's writing systems.
Next Class:
The Processor: Datapath, Pipelining & Instruction-Level Parallelism (Ch. 4)
Computer Architecture · Lecture 6
8