## Slide 1
COURSE: COMPUTER ARCHITECTURE
Input/Output Devices
Lecture 10 — Buses, Interfacing, Performance & RAID
Duration: 60 minutes
Reference: Patterson & Hennessy, Computer Organization and Design (4th Ed.), Ch. 6 §6.1, 6.5–6.7, 6.9

## Slide 2
Today's Agenda
Four building blocks for your tenth hour in Computer Architecture
01
I/O System Fundamentals
Dependability and cost come before raw performance
02
Five RAID Levels
Trading extra disks for performance and protection against failure
03
Polling vs. Interrupts
Two ways for a device to get the processor's attention
04
Measuring I/O Performance
Throughput, response time, and Amdahl's Law for I/O
Computer Architecture · Lecture 10
2

## Slide 3
I/O System Fundamentals
Connecting the processor to storage, networks, and people
Four Elements of an I/O System
I/O Device Types
Storage, networking, and human-interface devices each stress different metrics.
Dependability First
I/O systems are judged on dependability and cost before raw performance.
Buses & Interconnects
A shared set of wires — or switched serial links — connecting processor, memory, and I/O.
Interfacing to the CPU
Devices signal the processor by polling, interrupts, or DMA, coordinated by the OS.
Why I/O Design Matters
A bus's bandwidth caps total I/O throughput no matter how fast the individual devices are.
As processors get faster and more numerous, unchanged I/O time becomes a growing share of total time.
The operating system mediates I/O because multiple programs share the same devices.
Getting I/O wrong costs data, not just time — which is why dependability comes first.
Key idea: I/O systems are designed backward from processors: dependability and cost are the first priorities, with performance — throughput and response time — balanced against them rather than maximized alone.
Computer Architecture · Lecture 10 · Ch. 6 §6.1, 6.5–6.6 · pp. 570–595
3

## Slide 4
Five RAID Levels
Trading extra disks for performance and protection against failure
RAID 0
Striping — spreads data across disks for speed, with no redundancy at all.
no protection
RAID 1
Mirroring — writes every block to two disks; the most expensive, simplest scheme.
2× disks
RAID 3
Bit-interleaved parity — one dedicated parity disk protects all the others.
+1 disk
RAID 4
Block-interleaved parity — like RAID 3, but parity is computed per block, not per bit.
+1 disk
RAID 5
Distributed parity — spreads parity across all disks so small writes can happen in parallel.
widely used
Key idea: Every RAID level above 0 spends extra disks to survive a drive failure without losing data; the differences are in how much redundancy costs and how well small writes parallelize.
Computer Architecture · Lecture 10 · Ch. 6 §6.9 · pp. 599–604
4

## Slide 5
Polling vs. Interrupts
Two ways for a device to get the processor's attention
Polling
The processor periodically checks a status bit to see if a device needs attention
The simplest way for an I/O device to communicate with the processor
The processor's time is spent checking, whether or not there's work to do
Fine for devices that need attention very frequently
No extra hardware needed beyond a readable status register
Wastes cycles when the device rarely has work ready
Example use: simple embedded systems with few devices
Interrupts
The device signals the processor only when it actually needs attention
Lets the processor do other work while waiting for the device
Requires interrupt hardware and an operating-system handler
Better suited to devices that need attention only occasionally
Handling an interrupt has its own overhead — context must be saved and restored
Often paired with DMA for the actual data transfer
Example use: general-purpose operating systems and most modern devices
Computer Architecture · Lecture 10 · Ch. 6 §6.6 · pp. 586–592
5

## Slide 6
Measuring I/O Performance
Throughput and response time trade off against each other
Throughput
The total amount of work an I/O system completes per unit time.
Response Time
How long a single request takes from issue to completion.
The Trade-off
Batching requests together raises throughput but can increase response time.
DMA
Lets a device transfer data to or from memory directly, without the processor moving every word.
Amdahl's Law for I/O
If CPU time shrinks as processors get faster while I/O time stays fixed, I/O's share of total elapsed time grows — a program that's 90% CPU and 10% I/O today can become mostly I/O-bound after a few generations of faster processors.
Computer Architecture · Lecture 10 · Ch. 6 §6.7, 6.9 · pp. 596–599
6

## Slide 7
Where to Read More
Patterson & Hennessy — Computer Organization and Design, 4th Edition
Today's Topic | Book Section | Pages
I/O System Fundamentals | Ch. 6 — §6.1, 6.5–6.6 Introduction & Interfacing | 570–595
Five RAID Levels | Ch. 6 — §6.9 Parallelism and I/O: RAID | 599–604
Polling vs. Interrupts | Ch. 6 — §6.6 Interfacing I/O Devices | 586–592
Measuring I/O Performance | Ch. 6 — §6.7 I/O Performance Measures | 596–599
Also useful: Section 6.6, Interfacing I/O Devices, covers memory-mapped I/O and DMA in more depth; Section 6.12, Fallacies and Pitfalls, discusses common mistakes in estimating I/O performance.
Computer Architecture · Lecture 10
7

## Slide 8
Recap & What's Next
I/O systems are designed for dependability and cost first, with throughput and response time balanced second.
RAID levels trade extra disks for protection against drive failure, from simple mirroring to distributed parity.
Polling is simple but wastes cycles; interrupts let the processor do other work but cost handling overhead.
As processors get faster, unchanged I/O time claims a growing share of total elapsed time — Amdahl's Law applies to I/O too.
Next Class:
Course Wrap-Up: How ISA, Memory Hierarchy, Pipelining, Parallelism, and I/O Fit Together
Computer Architecture · Lecture 10
8