## Slide 1
COURSE: COMPUTER ARCHITECTURE
The Processor: Datapath, Pipelining & Hazards
Lecture 7 — Building the Datapath, the Five-Stage Pipeline, Data & Control Hazards
Duration: 60 minutes
Reference: Patterson & Hennessy, Computer Organization and Design (4th Ed.), Ch. 4 §4.3, 4.5, 4.7–4.8

## Slide 2
Today's Agenda
Four building blocks for your seventh hour in Computer Architecture
01
Datapath Fundamentals
The hardware that fetches, decodes, and executes an instruction
02
The Five-Stage Pipeline
Overlapping instructions like an assembly line
03
Data Hazards
Forwarding vs. stalling when instructions depend on each other
04
Control Hazards
Predicting branches and recovering when the guess is wrong
Computer Architecture · Lecture 7
2

## Slide 3
Datapath Fundamentals
The hardware elements every instruction passes through
Four Elements of the Datapath
PC & Instruction Memory
Holds the address of, then fetches, the next instruction to execute.
Register File
32 general-purpose registers; reads two operands and writes one result each cycle.
ALU
Performs arithmetic and logic operations, and computes branch and memory addresses.
Data Memory
Holds the values that load and store instructions read and write.
Why the Datapath Matters
Every instruction is fetched, decoded, and executed through the same shared hardware.
A single-cycle datapath is simple to reason about but forces the clock to match its slowest instruction.
Separate instruction and data memories let fetch and memory access happen without conflict.
The datapath's structure determines which instructions can safely overlap in a pipeline.
Key idea: The datapath is the physical hardware — registers, ALU, and memories — wired together to carry out one instruction; pipelining later overlaps several copies of this same hardware across neighboring instructions.
Computer Architecture · Lecture 7 · Ch. 4 §4.3 · pp. 307–315
3

## Slide 4
The Five-Stage Pipeline
Five stages, five instructions in flight at once
IF — Instruction Fetch
Read the instruction from memory and increment the program counter.
cycle 1
ID — Instruction Decode
Decode the opcode and read the register file.
cycle 2
EX — Execute
The ALU performs the operation or computes an address.
cycle 3
MEM — Memory Access
Load or store data in memory, if the instruction needs it.
cycle 4
WB — Write Back
Write the result back into the register file.
cycle 5
Key idea: With five instructions overlapped — one per stage — the pipeline completes roughly one instruction per cycle once it's full, even though any single instruction still takes five cycles start to finish.
Computer Architecture · Lecture 7 · Ch. 4 §4.5 · pp. 330–343
4

## Slide 5
Data Hazards: Forwarding vs. Stalling
Two ways to resolve a dependency between overlapping instructions
Forwarding
Routes a result directly from one pipeline stage to an earlier stage that needs it
Used whenever the needed value will be produced in time to route it
Adds extra data paths between pipeline stages
Costs no cycles — the pipeline keeps moving every cycle
Example: an ALU result forwarded straight into a dependent add
Resolves most data hazards in ordinary code
Cost: zero — built into the datapath as extra wiring
Stalling
Freezes the pipeline until the needed value is actually available
Used when the value isn't ready yet even with forwarding — e.g., right after a load
Needs hazard-detection hardware to insert a bubble
Costs one or more stall cycles every time it happens
Example: a load immediately followed by an instruction using its result
The compiler can also reorder code to avoid triggering it
Cost: one or more wasted cycles (a pipeline “bubble”)
Computer Architecture · Lecture 7 · Ch. 4 §4.7 · pp. 363–374
5

## Slide 6
Control Hazards & Branching
A branch's outcome isn't known until partway through the pipeline
Branch Detection
The pipeline must recognize an instruction is a branch before it knows which way it goes.
Predict Not Taken
The simplest static scheme: keep fetching sequentially, and flush if wrong.
Dynamic Prediction
A branch-prediction buffer records recent outcomes to guess before the branch resolves.
2-bit Predictor
Requires two wrong guesses in a row before changing its prediction.
Branch Hazards in Practice
In the classic five-stage MIPS pipeline, a mispredicted branch flushes the instructions fetched behind it — a real but modest penalty. In deeper, wider pipelines that penalty grows, which is exactly why aggressive designs lean more heavily on dynamic prediction.
Computer Architecture · Lecture 7 · Ch. 4 §4.8 · pp. 375–383
6

## Slide 7
Where to Read More
Patterson & Hennessy — Computer Organization and Design, 4th Edition
Today's Topic | Book Section | Pages
Datapath Fundamentals | Ch. 4 — §4.3 Building a Datapath | 307–315
The Five-Stage Pipeline | Ch. 4 — §4.5 An Overview of Pipelining | 330–343
Data Hazards: Forwarding & Stalling | Ch. 4 — §4.7 Forwarding vs. Stalling | 363–374
Also useful: Section 4.9, Exceptions, and Section 4.13, Fallacies and Pitfalls, round out how real pipelines handle the unexpected.
Computer Architecture · Lecture 7
7

## Slide 8
Recap & What's Next
The datapath is shared hardware — PC, register file, ALU, and memories — that a pipeline overlaps across several instructions at once.
A five-stage pipeline (IF, ID, EX, MEM, WB) approaches one instruction per cycle once it's full, even though each instruction still takes five cycles.
Forwarding resolves most data hazards for free; a load-use hazard still needs a stall cycle.
Control hazards are handled by predicting the branch outcome and flushing the pipeline when the prediction is wrong.
Next Class:
Parallelism & Instruction-Level Parallelism: Multiple Issue, Speculation & Dynamic Scheduling (Ch. 4 §4.10)
Computer Architecture · Lecture 7
8