## Slide 1
COURSE: COMPUTER ARCHITECTURE
Parallelism & Instruction-Level Parallelism
Lecture 8 — Multiple Issue, Speculation, and Dynamic Scheduling
Duration: 60 minutes
Reference: Patterson & Hennessy, Computer Organization and Design (4th Ed.), Ch. 4 §4.8, §4.10

## Slide 2
Today's Agenda
Four building blocks for your eighth hour in Computer Architecture
01
Instruction-Level Parallelism
Pushing more instructions through the pipeline than one at a time
02
Techniques That Raise ILP
Deeper pipelines, multiple issue, VLIW, and loop unrolling
03
Static vs. Dynamic Scheduling
Who decides the instruction order: the compiler or the hardware?
04
Dynamic Scheduling in Hardware
Reservation stations, register renaming, and the reorder buffer
Computer Architecture · Lecture 8
2

## Slide 3
Instruction-Level Parallelism: The Basics
Finding more independent work for the pipeline to do
Four Ideas Behind ILP
What Is ILP?
The parallelism among instructions in a single program, available for hardware or software to exploit.
Deeper Pipelining
Split pipeline stages further so more instructions overlap, once the stages are rebalanced.
Multiple Issue
Replicate hardware to launch more than one instruction per clock cycle.
Speculation
Guess past an unresolved branch or hazard and execute ahead, undoing the work if wrong.
Why ILP Matters
Real programs rarely fill a single-issue pipeline every cycle, so there's headroom to exploit.
Multiple issue can be done by the compiler (static) or by the hardware itself (dynamic).
Speculation lets the processor keep working instead of waiting for a hazard to resolve.
The limits of ILP — not clock speed alone — have shaped processor design since the 1990s.
Key idea: Instruction-level parallelism is parallelism that already exists among nearby instructions in ordinary code; processors exploit it by going deeper, wider, or both, then use speculation to keep the pipeline full despite hazards.
Computer Architecture · Lecture 8 · Ch. 4 §4.10 · pp. 391–393
3

## Slide 4
Five Techniques That Raise ILP
From one instruction per cycle to several
Deeper Pipelining
More, shorter pipeline stages let more instructions overlap.
5 → 8+ stages
Static Multiple Issue
The compiler packs multiple instructions into each issue slot ahead of time.
VLIW
Dynamic Multiple Issue
The hardware itself decides which instructions to issue together each cycle.
superscalar
Loop Unrolling
The compiler repeats a loop body to give itself more independent work to schedule.
×4 unroll
Register Renaming
Extra physical registers remove false dependencies between instructions.
WAR/WAW gone
Key idea: None of these techniques create parallelism that wasn't already in the program — they just get better at finding and exploiting it, whether at compile time or run time.
Computer Architecture · Lecture 8 · Ch. 4 §4.10 · pp. 391–398
4

## Slide 5
Static vs. Dynamic Multiple Issue
Who schedules the instructions: the compiler or the hardware?
Static Multiple Issue
The compiler decides which instructions issue together, ahead of time
Used by VLIW (Very Long Instruction Word) designs
Simpler hardware — no runtime scheduling logic needed
Relies on the compiler to find independent instructions
Example: MIPS-based embedded two-issue processors
Loop unrolling is the compiler's main tool here
Example use: embedded and low-power designs
Dynamic Multiple Issue
The hardware decides at runtime which instructions issue together
Used by superscalar designs
More complex hardware — needs scheduling and hazard-detection logic
Can reorder instructions around unpredictable stalls, like cache misses
Example: reservation stations feeding multiple functional units
Register renaming removes false dependencies automatically
Example use: most general-purpose desktop and server processors
Computer Architecture · Lecture 8 · Ch. 4 §4.10 · pp. 391–392, 401–403
5

## Slide 6
Dynamic Scheduling in Hardware
How out-of-order processors reorder instructions safely
Reservation Stations
Buffer an instruction and its operands until they're ready to execute.
Out-of-Order Execution
Instructions execute as soon as their operands are ready, not in program order.
Register Renaming
Reservation stations give each result its own physical location, removing false dependencies.
Reorder Buffer & Commit
Results are held until it's safe to commit them in the original program order.
Dynamic Scheduling in Practice
Dynamic scheduling pays off in two ways a compiler can't: it hides unpredictable stalls like cache misses by continuing other work, and if the processor speculates on a branch, it can discard speculated instructions without ever committing their results.
Computer Architecture · Lecture 8 · Ch. 4 §4.10 · pp. 399–401
6

## Slide 7
Where to Read More
Patterson & Hennessy — Computer Organization and Design, 4th Edition
Today's Topic | Book Section | Pages
Instruction-Level Parallelism: The Basics | Ch. 4 — §4.10 Parallelism and Advanced ILP | 391–393
Five Techniques That Raise ILP | Ch. 4 — §4.10 Parallelism and Advanced ILP | 391–398
Static vs. Dynamic Multiple Issue | Ch. 4 — §4.10 Parallelism and Advanced ILP | 391–403
Dynamic Scheduling in Hardware | Ch. 4 — §4.10 Parallelism and Advanced ILP | 399–401
Also useful: Section 4.8, Control Hazards, covers the branch prediction that speculative processors depend on; Section 4.13, Fallacies and Pitfalls, discusses the practical limits of multiple issue.
Computer Architecture · Lecture 8
7

## Slide 8
Recap & What's Next
Instruction-level parallelism is the independent work already present among nearby instructions in ordinary code.
Processors exploit it with deeper pipelines, multiple issue (static or dynamic), and speculation.
Static multiple issue leans on the compiler; dynamic multiple issue lets the hardware reorder instructions at runtime.
Reservation stations, register renaming, and the reorder buffer let hardware execute out of order while still committing results in program order.
Next Class:
Multiprocessors & Multi-core Computers: Shared Memory, Message Passing & Flynn's Taxonomy (Ch. 7)
Computer Architecture · Lecture 8
8