## Slide 1
COURSE: COMPUTER ARCHITECTURE
Multiprocessors & Multi-core Computers
Lecture 9 — Parallel Hardware, Shared Memory & Flynn's Taxonomy
Duration: 60 minutes
Reference: Patterson & Hennessy, Computer Organization and Design (4th Ed.), Ch. 7 §7.1, 7.3–7.6

## Slide 2
Today's Agenda
Four building blocks for your ninth hour in Computer Architecture
01
Why Parallel Hardware?
Power limits pushed the industry from faster cores to more cores
02
Flynn's Taxonomy
Five classes of parallel hardware, from SISD to Vector
03
Shared Memory vs. Message Passing
Two ways for processors to cooperate on the same problem
04
Multicore & Multithreading
Packing more processors — and more threads — onto one chip
Computer Architecture · Lecture 9
2

## Slide 3
Why Parallel Hardware?
The shift from faster uniprocessors to more processors
Four Drivers of Parallel Hardware
Power Efficiency
Many smaller, efficient cores can deliver better performance per watt than one large core.
Task-Level Parallelism
Running genuinely independent jobs or threads side by side on separate processors.
Data-Level Parallelism
Applying the same operation to many data elements at once.
The Programming Challenge
Writing correct, fast parallel programs is far harder than writing sequential ones.
Why This Shift Matters
Clock speeds stopped growing rapidly once power and heat became the limiting factor.
Amdahl's Law still applies: the serial fraction of a program bounds the speedup, however many cores are added.
Not all problems parallelize equally well — some hardly at all.
This is why “multicore” became the default answer to “how do we make chips faster?”
Key idea: When single cores stopped getting dramatically faster, the industry turned to adding more of them — trading the hard problem of making one processor faster for the hard problem of writing software that can use many processors at once.
Computer Architecture · Lecture 9 · Ch. 7 §7.1–7.2 · pp. 632–637
3

## Slide 4
Flynn's Taxonomy: Five Classes of Hardware
Classifying hardware by its instruction and data streams
SISD
Single instruction, single data — the conventional uniprocessor.
1 core
MIMD
Multiple instruction, multiple data — independent streams; most multiprocessors and multicores.
N cores
SIMD
Single instruction, multiple data — one operation applied across many ALUs at once.
×N lanes
SPMD
Single program, multiple data — every processor runs the same program on its own data, not in lockstep.
MIMD style
Vector
A single instruction operates on an entire sequence of data elements pipelined through one unit.
v[0..n]
Key idea: SISD and MIMD classify hardware by whether there's one instruction stream or many; SIMD, SPMD, and Vector are three different ways to apply one instruction stream's worth of control to lots of data at once.
Computer Architecture · Lecture 9 · Ch. 7 §7.6 · pp. 648–653
4

## Slide 5
Shared Memory vs. Message Passing
Two ways for processors to cooperate on a problem
Shared Memory Multiprocessors
All processors share one physical address space
Communication happens implicitly through ordinary loads and stores
UMA: access time to memory is uniform for every processor
NUMA: access time depends on which memory bank a processor is near
Needs cache-coherence hardware to keep shared data consistent
Programming model is familiar, but synchronization (locks) is required
Example use: symmetric multiprocessor (SMP) servers
Message-Passing Multiprocessors
Each processor has its own private memory
Communication happens explicitly by sending and receiving messages
No shared address space, so no cache-coherence hardware is needed
Naturally suits clusters of separate machines connected by a network
Programming model is more explicit, but often easier to reason about
Scales to very large numbers of processors — even entire clusters
Example use: warehouse-scale clusters and supercomputers
Computer Architecture · Lecture 9 · Ch. 7 §7.3–7.4 · pp. 638–644
5

## Slide 6
Multicore & Hardware Multithreading
Packing more processors — and more threads — onto one chip
Multicore Chips
Multiple complete processors fabricated on a single chip, sharing an interconnect and outer cache.
Coarse-Grained Multithreading
Switches between threads only on a costly stall, such as a cache miss.
Fine-Grained Multithreading
Switches between threads every clock cycle, hiding both short and long stalls.
Simultaneous Multithreading
Issues instructions from multiple threads in the very same clock cycle.
Multithreading in Practice
Hardware multithreading doesn't add processors — it lets one processor's pipeline stay busy by switching to a different thread's instructions whenever the current thread is stalled, squeezing more useful work out of the same hardware.
Computer Architecture · Lecture 9 · Ch. 7 §7.5 · pp. 645–647
6

## Slide 7
Where to Read More
Patterson & Hennessy — Computer Organization and Design, 4th Edition
Today's Topic | Book Section | Pages
Why Parallel Hardware? | Ch. 7 — §7.1–7.2 Introduction | 632–637
Flynn's Taxonomy: Five Classes of Hardware | Ch. 7 — §7.6 SISD, MIMD, SIMD, SPMD, Vector | 648–653
Shared Memory vs. Message Passing | Ch. 7 — §7.3–7.4 Multiprocessors | 638–644
Multicore & Hardware Multithreading | Ch. 7 — §7.5 Hardware Multithreading | 645–647
Also useful: Section 7.7, Introduction to Graphics Processing Units, extends SIMD/SPMD ideas to the GPU; Section 7.13, Fallacies and Pitfalls, covers common misconceptions about parallel speedup.
Computer Architecture · Lecture 9
7

## Slide 8
Recap & What's Next
Power limits, not a lack of transistors, pushed processor design from faster uniprocessors toward multiple cores.
Flynn's taxonomy — SISD, MIMD, SIMD, SPMD, and Vector — classifies hardware by its instruction and data streams.
Shared-memory multiprocessors communicate through loads and stores; message-passing multiprocessors communicate explicitly and scale further.
Multicore chips and hardware multithreading are two different ways to put more execution capacity on the same die.
Next Class:
Input/Output Devices: Buses, Interfacing, Performance & RAID (Ch. 6)
Computer Architecture · Lecture 9
8